## Slide 1
S100WG5 Papers 4.15
Validation Checks for GML and HDF5 Data Formats S-100 WG5 3-6 March 2020 4.15 A/B/C

## Slide 2: Overview
Outline of a specification of generic validation checks for S-100 GML and HDF5 data formats.
  Specification will be defined at the “S-100 level”.
  Whether the specification will be a new S-100 Part or sub-Part, an Annex to Part 10, or a separate document (like S-58 is for ENC checks) is TBD at this point.
The submission includes illustrative examples of HDF5 and GML checks.
  The S-111 checks incorporate feedback from the S-111 project team & developers & should be in the next S-111 draft.
  The S-127 checks are from the S-127 1.0.0 package reviewed by NIPWG.
Individual Product Specifications are expected to include and extend the core sets of checks as appropriate.

## Slide 3: Documentary components
Derived from S-58 (S-57 ENC validation checks), with extensions for S-100 GML and HDF5 data formats.
The main components of the planned specification are:
  A “core specification” for validation, describing:
    Check classification(s): e.g., critical/error/warning.
    Description of check syntax.
    Check application (e.g., base/update datasets – for GML in particular).
    Operators (comparison, logical, and spatial).
    Check processing flow (for HDF5 in particular, requested by the S-111 project team & developers).
  Generic checks for the S-100 Part 10c HDF5 data format.
  Generic checks for the S-100 Part 10b GML data format.
Individual Product Specifications are expected to extend the core specification and generic validation checks as needed.

## Slide 4: Actions requested
Endorse the development of generalized validation checks for the S-100 GML and HDF5 formats as described in this paper and the accompanying Annexes.
Subject to item (1), advise on any special requirements for other product specifications.
Additional action as appropriate.

## Slide 5
S100WG5 Papers 4.20, 4.21, 4.22

## Slide 6: Activity for S-100 WG4 4.2
Action 3 activity: Proposal WG4 4.12 updated.
  Proposal updated in consultation with S-102 & S-111 product specification development teams.
  Guidance on use of file families added.
  Another option for exchange set metadata to describe file families.
Action 5 activity: Proposal WG4 4.14 revised & split.
  Proposal updated in consultation with S-102 & S-111 product specification development teams.
  Added use cases for data offset code and offset vector to proposal justification.
  Four “corners” are retained because allowing only one “corner” is ambiguous and over-constrained given the variations possible in encoding of grid origin & scan direction in the HDF5 format.
Action 6 activity: Proposal WG4.14 revised & split.
  Clarifications for 10c are pulled out into a separate proposal.
  Minor change to language in 10c-9.3.
  New dataCodingFormat=8 in anticipation of action on WG5 4.18 (extensions to HDF5).
All actions: Proposed revisions to Part 8 (Imagery ...) have been removed pending action on the proposed holistic review of Part 8 (WG5 6.6).

## Slide 7: Status of S-100 WG4 Actions 3, 5, 6
Action 3 (file families):
  Action completed.
  Revised proposal developed in consultation with PS development teams.
  To be discussed at WG or TSM?
Action 5 (data offset code & vector):
  Action completed.
  Revised proposal developed in consultation with PS development teams.
  To be discussed at WG or TSM?
Action 6 (clarifications to Part 10c):
  Action ongoing.
  All but one of the revisions are clarifications and were discussed at WG4.
  The single extension (enumeration member for DCF=8) is new. It anticipates action on WG5 4.18.