## Slide 1: Alerts and Indications Model for S-100 (proposed)
Presented by SPAWAR
for TSM6
Sept 2018

## Slide 2: Background
TSMAD28 & TSM3
Hannu presented the need for an alert model defined within S-100
Allow fielded ECDIS systems to respond to changes in alert requirements without software upgrades
Addition of alerts from emergent product types
Addition of new feature types which generate alerts
Changes to pre-existing alert processing rules
Notes: Identified by Svein Skjæveland of ECC

## Slide 3: Background
S100WG01-10.12A
Alert model based on portrayal model
Portrayal Model: Encoded dataset => drawing instructions
Alert Model: Encoded dataset => alert instructions
Notional model based on XSLT rule files
Alert Instructions
Identify one or more spatial elements of an encoded dataset to be evaluated by ECDIS alert processing
Does not provide spatial processing (manufacturer responsibility)
No provision for alerts not generated from a spatial element of a dataset
Deviation from route
Positioning system failure
etc.

## Slide 4: References
IEC
61174:2015 – ECDIS performance requirements
62288:2014 – Presentation of navigation information on shipborne navigational displays
62616:2010 – Bridge navigational watch alarm system (BNWAS)
IMO
Assembly
A.1021(26) – Code on alerts and indicators, 2009
Maritime Safety Committee
MSC.302(87) – Adoption of Performance Standards for Bridge Alert Management
MSC.252(83) – Revised performance standards for INS
MSC.232(82) – Revised performance standards for ECDIS

## Slide 5: Definitions
Alert: Announces abnormal situations requiring attention
Priority
Alarm: Highest priority of alert. Condition requiring immediate attention and action by the bridge team, to maintain the safe navigation of the ship.
Warning: Condition requiring no-immediate attention or action by the bridge team. Warnings are presented for precautionary reasons to make the bridge team aware of changed conditions which are not immediately hazardous, but may become so, if no action is taken.
Caution: Lowest priority of alert. Awareness of a condition which does not warrant a alarm or warning condition, but still requires attention out of the ordinary consideration of the situation or of given information.
Category
A: Graphical information at the task station directly assigned to the function generating the alert is necessary, as decision support for the evaluation [of] the alert related condition.
B: No additional information for decision support is necessary besides the information which can be presented at the central alert management HMI
Indication: Display of regular information and conditions, not part of alert management
Permanent Indication: Indication not to be removed from the display
Other informal terms are used: e.g. “clear indication”
Notes: Indications are typically used to indicate status

## Slide 6: Required Model Components
Alert
“Crossing safety contour”
Mechanism to disable trigger
“Selector”
What happens to active alerts when disabled
E.g. Disable anchor watch – active alerts should be cleared
Priority
Category
Message (text)
A location for the message
An icon (optional?)
Alarm
Warning
Caution
A
B
Trigger condition
Notes: Required components are based on preceding references

## Slide 7: Required Model Components
Alert
A fill symbol (for areas)
A line style (for areas and lines)
A point symbol (for points)
The geometry of the highlight (e.g. intersection of feature and route)
Display plane and drawing priority are not currently included
Mechanism to disable the highlight
“Selector”
An indication displayed when / while the highlight is disabled
Display on demand components
E.g. “Crossing safety contour” alert requires display of “feature and highlight” on demand
Graphical Highlight – displayed while alert is active

## Slide 8: Required Model Components
Indication
An icon (optional?)
Type of indication
Location of indication
Generally not specified in references, overlaying chart assumed
Imprecise in some references, e.g. “Close to north arrow”
Display on demand components
E.g. “AIS target filter enabled” requires display of “AIS target filter criteria” on demand
Route planning checks treat “Indication” as an alert priority
Requires graphical highlighting with mechanism to disable
Indication message (text)
Permanent
Non-permanent?

## Slide 9: Design Goals
Eliminate the need for ECDIS software changes due to hard-coding of requirements
Model all alerts and indications, not just those triggered by encoded dataset features
Model all components necessary to implement alerts and indications
Added layers can use the alerts model
User-drawn no-go areas
Enable flexible HMI implementation
Provide language independent text
Provide icons / symbols to minimize screen space required / language issues
ref. IEC 61174:2015 Annex N

## Slide 10: Design Limitations
Display on demand
Unbounded requirements
Modeled as strings
Add existing requirements as enumerations?
Association of alerts with trigger conditions
Alerts generated from encoded feature geometries share a single software module; new alerts can be added with no ECDIS software changes
Other associations must be coded as individual modules within the ECDIS; new alerts require new code to associate a trigger condition with a catalogue entry
Pre-existing alerts can be changed with no ECDIS software changes
XML alert instructions
Augmented geometries can only be used if generated by the portrayal
Lua alert instructions do not have this restriction
Not modeled
Interoperability
Audible alert signals

## Slide 11: Design Approach
S100WG01-10.12A
S-100 Part X
S-100 Part 4
Associate alert catalogue with a FC and PC
facilitate delivery of alert catalogue
Alerts and indications

## Slide 12: Design Approach
Current approach
Model alerts as part of the portrayal
Doesn’t require a new S-100 part
Leverages the portrayal for delivery of the alert catalog
Can use existing portrayal mechanisms to provide symbols and line styles for highlighting
Generation of alert instructions requires minimal changes to existing portrayal rules
No new builder tool required
Modify PCB to associate a feature with an alert catalogue entry
XSLT and Lua have common model / implementation
Alert instruction generated by portrayal is the only difference
Provide alerts to the ECDIS via an alert catalogue
Plagiarize interoperability concept
Delivered as a file reference from portrayal catalogue
Same model for XSLT and Lua
XML catalogue
Allows delivery of alerts which are not triggered by encoded geometries

## Slide 13: Model Overview
Alert catalogue is provided as a component of the portrayal catalogue
Alert catalogue provides alerts, indications, and other required components
Portrayal rules generate drawing instructions which can associate encoded geometries with alert catalogue entries
Portrayal Rule
Alert Catalog Entry
Drawing Instruction

## Slide 14: Required Changes to Part 9
Add alertCatalog to FileType (type of an external file)
Add alertCatalog to PortrayalCatalog
Adds an external file reference as an entry in the PortrayalCatalog.xml
Add class AlertReference
alertReference attribute specifies an alert in the alert catalog
Optional highlightSelector attribute specifies an alert catalog selector entry
Used to disable a graphical highlight on a per-feature basis
Supports requirements for areas with special conditions
Add alertReference to DrawingInstruction class
Multiplicity: 0..1
Type: AlertReference
Adds optional alert catalog reference to all drawing instructions
Notes: Areas with special conditions can have graphical highlighting disabled separately for each feature type.
Because alertReference shares the DrawingInstructions featureReference and spatialReference it is not possible to alert on augmented geometries unless they are also portrayed. An alert instruction could be added which contains its own feature and spatial references, allowing alerting on arbitrary geometries at the expense of slightly more complicated portrayal rules.

## Slide 15: Required Changes to Part 9a
Add 9a-11.2.x Alert Commands
AlertInstruction:alertReference[,highlightSelector]
Instructs the host to include the referenced geometries in alert processing
alertReference: Reference to an alert in the alert catalog
highlightSelector: If present, references a selector in the alert catalog used to disable the graphical highlight
Alert commands are modified by preceding Geometry state commands
Supports alerting on augmented (soundings) or component (safety contour) geometries
Notes: Because Geometry state commands can precede or follow the alertReference the AlertInstruction can alert on augmented geometries independently of portrayal.

## Slide 16: Model of the Alert Catalog
The alert catalogue provides all required components other than the trigger condition
Single trigger condition for alerts associated with encoded geometries
Can be associated with any number of catalog entries based on rules implemented within the portrayal
Individual trigger conditions for all other catalogued alerts
Implementation is a manufacturer responsibility
Alert catalog provides all required components, but there is no dataset feature to trigger the alert
ECDIS must lookup the entry associated with the trigger condition.
On positioning system failure => lookup catalog entry “PositioningSystemFailure”

## Slide 17: Model of the Alert Catalog

## Slide 18: Model of the Alert Catalog

## Slide 19: Contents of the Alert Catalog
Context Parameters
Parameters affecting the generation of alerts and indications
Portrayal context parameters are also available to alerts
Alert context parameters do not alter chart rendering
Avoid use
Context parameter change => re-generate drawing instructions
Not used by sample S-101 alert catalog
Use case for other product types?
Messages
Language independent text referenced from alerts and selectors
Notes: Could add a disabled/deactivatedSelectionValue to permit deactivation of non-Boolean selectors

## Slide 20: Contents of the Alert Catalog
Selectors / Selector: Select one of many values. Usually Enabled or Disabled, e.g. graphical highlight or alert trigger
Name | Description |  | Type
type | e.g. Boolean. Consider adding: anyURI, time, dateTime, duration, language | 1 | ParameterType
icon | A symbol from the portrayal catalog | 0..1 | Reference
label | Language independent text describing the selector | 1..* | Text
indicationWhenDisabled | An indication to display when the selector is disabled. Only used with Boolean selectors. | 0..1 | Reference
clearOnDeactivation | Indicates whether active alerts should be cleared. Only used with Boolean selectors. | 0..1 | Boolean
dependency | This selector can only be enabled when other selectors are enabled. | 0..* | DependencyType
selection | The selections of the selector. | 2..* | Selection

## Slide 21: Contents of the Alert Catalog
Selection: A single choice for a Selector
Name | Description |  | Type
default | If true, indicates the default selection | 0..1 | Boolean
icon | A portrayal catalog symbol | 0..1 | Reference
message | The text of the selection | 1 | Reference
value | The value of the selection. Static / Immutable | 1 | anyType
indication | Indication enabled when / while the selection is selected | 0..1 | Reference

## Slide 22: Contents of the Alert Catalog
Alerts / AlertItem: Describes each alert
  selector (0..1): Reference to a selector used to enable the alert
  priority / prioritySelector:
    The alert priority (Alert, Warning, Caution, PermanentIndication, Indication) -or-
    a reference to a selector whose selection identifies the alert priority
  category (0..1): A or B
  escalateSeconds (0..1): nonNegativeInteger. Override for default escalation.
    Ref. MSC252(83) 20.5 Alert Escalation
  trigger (0..1): Spatial check which triggers the alert
    E.g. Intersection: check for intersection of feature with look-ahead / route plan
  message: Reference to a Message to display while alert is active
  icon (0..1): Displayed with / instead of the message
    Message should still be available – e.g. hover over icon
Name | Description |  | Type
selector | A selector used to enable / disable the alert | 0..1 | Reference
priority | Alarm, Warning, …, PermanentIndication, Indication | 1 | AlertPriority
prioritySelector | A selector used to set the alert priority |  | Reference
category | A or B | 0..1 | AlertCategory
escalateSeconds | Override for default escalation (ref. MSC252(83) 20.5 Alert Escalation) | 0..1 | nonNegativeInteger
trigger | Spatial check which triggers the alert (e.g. Intersection) | 0..1 | SpatialCheck
message | Message to display while alert is active | 1 | Reference
icon | A portrayal catalog symbol. Message via hover? | 0..1 | Reference
messageLocation | Where to display the message / icon (e.g. AlertManagement) | 1 | MessageLocation
highlight | Describes how to highlight the source of the alert | 0..1 | GraphicalHighlight
displayOnDemand | A list of display on demand requirements (ref. earlier comments) | 0..* | string
Notes: Ref. MSC252(83) 20.5 Alert Escalation. Specifies escalation time in seconds per performance standards.
Unacknowledged alarms escalate to the BNWAS, if available.
Unacknowledged warnings escalate to alarms.
It is unclear if escalated warnings should be further escalated to the BNWAS.

## Slide 23: Contents of the Alert Catalog
GraphicalHighlight: Describes how to highlight an alert or indication
Name | Description |  | Type
display | How the highlight should be displayed. Intersection of source with identified geometries (ref. IEC 62288:2014, Table A.3) | 1 | GraphicalDisplayType
pointSymbol | A portrayal catalog symbol | 0..1 | Reference
lineStyle | A portrayal catalog LineStyle | 0..1 | Reference
areaFill | A portrayal catalog AreaFill | 0..1 | Reference
selector | An alert catalog selector used to enable / disable the highlight | 0..1 | Reference
Notes: Ref. MSC252(83) 20.5 Alert Escalation. Specifies escalation time in seconds per performance standards.
Unacknowledged alarms escalate to the BNWAS, if available.
Unacknowledged warnings escalate to alarms.
It is unclear if escalated warnings should be further escalated to the BNWAS.

## Slide 24: Companion Package
AlertRequirements.xlsx
AlertCatalog.EAP – Enterprise architect file generated from AlertCatalog.xsd
AlertCatalog.svg – Interactive UML model generated from AlertCatalog.xsd
View using Google Chrome
Initial requirements analysis
AlertCatalog.xml
Sample implementation (incomplete) of an alert catalog for S-101
XML Schemas (.xsd files)
AlertCatalog – The model of the alert catalog
S100Presentation – Full schema modified to support alerts
S100PresentationChanges – Summarizes changes to S100Presentation
S100PortrayalCatalog – Full schema modified to support alerts
S100PortrayalCatalogChanges – Summarizes changes to S100PortrayalCatalog
S100SymbolDefinition – Unchanged, provided to support validation
S100CSL.xsd – Unchanged, provided to support validation
UML

## Slide 25: Conclusion
The model presented addresses the design goals within the defined limitations
Are the limitations acceptable?
Should work continue using the approach presented?
Implementation outside of portrayal will require significant additional work
Next step using current approach is a complete sample implementation for S-101
AlertsRequirements.xlsx shows many details remain
Mainly requirements clarifications
No anticipated affect on the model presented
Can be addressed through iterative refinement of an alert catalog implementation