## Slide 1
Shortcomings of the current Part 10b.
The approach in Part 10b is to manually define a GML Application Schema using the collection of definitions in the part. This requires an additional, predominantly manual step in the creation of a product specification, following the model and feature catalogue creation. Much of the content in a GML Application Schema is replicated (albeit in XML Schema form) from the feature catalogue.
Some of the content is now outdated and IHO-specific, for example DSID information, FOID identifiers and coordinate multiplication factors.
Options are introduced which hinder automatic parsing of GML files and extraction of feature and information types. There is ambiguity within GML Application Schemas created under the profile due to these options. Examples are naming of associations/roles and adoption of labels/values for listed values in schemas.
Proposal:
Modernise content and bring it in line with other parts of S-100. Take out outdated elements. Increase interoperability of “S-100 GML” with mainstream GI tools and technologies.
Reduction of the amount of “leeway” offered within the profile in the construction of GML Application Schemas. This would make the profile more tightly defined and make the mapping from a product specification feature catalogue to its GML application schema one-to-one.
The extension of the GML profile to better cover the construction of datasets from individual feature and information types.
S-100 GML Revision

## Slide 2
A defined mapping from the S-100 primitive types to GML types
Standardisation of GML schema element naming. Explicit mapping of the names/codes defined in the feature catalogue to the GML elements for
  Features and Information types
  Attributes and sub-attributes including multiplicities and listed values
  Associations and roles
Standardisation of GML dataset layout and feature collection methodology.
Removal of outdated items:
  DSID metadata where not required
  DSPM items including feature/geometry counts and coordinate/sounding multiplication factors.
  FOID, in place of MRN (as a feature attribute) and gml:id as the unique identifier within GML datasets.
A tighter selection of GML geometry primitives to be used and the mapping of those primitives to the geometry levels specified in S-100 Part 7
Where options are still allowed, a default will be specified and a configuration parameter in metadata will denote the choice selected (e.g. value codes/labels in listed value encodings)
Interoperability with broader GIS technologies:
  Use of standard GML types where possible, instead of S-100 extensions (e.g. removal of generic associations)
  Removal of S-100 quirks, e.g. coordination multiplication factors
  Standardisation of feature collection forms and syntax
  Settling on v3.2.1 which has widespread adoption among implementers
The requirement of “precedence” to ensure entities are named before use is not required by GML itself and should not be a constraint on the GML profile.
The insertion of more complete, normative example features and datasets for use by implementers. This will be accompanied by the installation of the revised GML profile within the IHO website for online validation.
S-100 GML Revision